## Slide 1: Assignments Schedule: Breakout game Stage A/1
Row numbers can vary a bit from the values below.
Demonstrate operation using a few annotated screen captures
Use 32-bit data memory rows 0 – 15 as game arena
Paddle in word 2, with centre point at bit 16
Wall in word 15
Score in word 2, number of lives in word 1 (=3 at start)
Ball in row 3 start, bit 16
Vertical ball movement only
Increment score when wall element is removed by ball
No of lives will always be 3, i.e, can’t end the game with lives = 0
Use functions where useful
Design documentation highlighting program structure, register assignment

## Slide 2: Assignment: Breakout game submission stage B/2
RISC-V breakout game arena / IDE
High quality game design documentation. Include complete header page.
Structured assembly program, with clear and efficient commenting
Implement and demonstrate (video) and upload to BB
List and detail of any issues (resolved or unresolved)
Zip program and upload to BB
Assessment considers functionality and clarity of design documentation and code
Bonus options:
  Highlight game over / message
  Game start control using IOIn(2) input toggle low-high-low
  Increase speed after score = 5 and 10
  Add two wall rows with (space between) in rows 12 and 15
  Other self-proposed function (highlight and document)

## Slide 3: EE451 RISC-V Assignments Schedule
Title Submission date
swapX3DigitX4WithX5DigitX6 Tuesday 26th Oct
Breakout game Stage A Tuesday 8th Nov
Breakout game Stage B Tuesday 21st Nov

## Slide 4
Assignment: Breakout game submission

## Slide 5: Ball rebound strategy
Left (In Vector) highlights the incoming direction of the ball when it hits the paddle
Columns left, middle and right highlight the required rebound direction on ball collision with paddle.

## Slide 6: RV32I RISC-V Instruction Examples
Course contents and links (on vicilogic)
RISC-V breakout game arena / IDE
RV32I RISC-V base instruction set
vicilogic RV32I RISC-V IDE Assembly programming IDE and sandbox (integrated development environment)
  Download RV32I instruction example programs, copy/paste, assemble,execute and test
Venus online RISC-V assembly program simulator https://venus.kvakil.me/
RISC-V RV32I Instruction generator
3

## Slide 7: Points discussed at class 1st Nov
Use of functions
  If using nested function calls
    use push/pop approach to/from stack, to perform return address house-keeping
  Do not branch from one function to another
  Only use branches in a contiguous code section.
  If calling a function using jal, recommended to use rd = x1
  Don’t use rd = x0 in function call
  The above adheres to a formal process and supports function re-use

## Slide 8: Points discussed at class 1st Nov
Template RISC-V .s program
  Structure, register allocation, some function code
is available on BB for reference (use
GameApplication_V1.1_template.s RISC-V template provided on BB
Include assembly program structure which you may wish to consider (all, part of, or none)
Includes register allocation. Include your allocation in your solution.
Uses NS* and CS* variables, though as discussed in class, you can do without using NS* variables in your solution

## Slide 9
vicilogic breakout game
RISC-V: Consider the following variables and possible register assignment

## Slide 10: RV32I RISC-V Instruction Index / Course Modules
RV32I RISC-V Level II Instruction Set Index
RV32I RISC-V Level I Instruction Set Index

## Slide 11: Assignment: Breakout game Stage A
Use main memory words 0 – 15 as game arena
  Paddle row 2, with centre point at bit 16, 5-bit wide
  Wall row 15
  Ball start position row 3, bit 16
  Score row 1
  Number of remaining lives row 0, initialise with 3
Stage A: implement vertical ball movement only and not moving paddle
  The number of lives will always be 3, since cannot end the game
Increment score when ball collides with active wall element
Lose life when ball passes paddle (on downward movement)
Game over when number of lives = 0

## Slide 12: Assignment: Breakout game Stage A
Use functions
  Try to avoid nested function
  If using nested function, refer to vicilogic lesson
Preparation and documentation
  Game strategy / functions
  Register allocation and function
  Game memory addressing

## Slide 13: Assignment: Breakout game Stage B
Paddle left / right movement
  Controlled by RISC-V processor input port signal IOIn(1:0) (L:R)
  Memory address 0x00030008
  Use RISC-V lw rd, imm(rs1) instruction

## Slide 14: Assignment: Breakout game Stage B
Support angled movement, with 0, 45, 90 degree movement directions
  If ball touches paddle on down movement
    Vertical direction
      touching left paddle bit rebound in up, NW direction
      touching right paddle bit rebound in up, NE direction
    SW direction
      touching right paddle bit rebound in up, N direction
    SE direction
      touching left paddle bit rebound in up, N direction
    Other down E-W directions
      rebound in up, W-E direction direction

## Slide 15: Assignment: Breakout game Stage B
wall collision handling

## Slide 16: Breakout game zones
Zone regions